## Slide 1: From Menace to Meals

## Slide 2: How Legislative support has turned Fire
into Food

## Slide 3: Natural density of old growth forest surrounding Tok

## Slide 4: Brief History / including series of fire threats and community evacuations
100 year old climactic forest.
1000 strikes per day.
5 major fires / million acres plus/ 3 major community exits.
Over 100 million spent on fighting fires.

## Slide 5: Proper Forest management showing selective thinning

## Slide 6: Summary of the Forestry standards applied through selective thinning and harvesting
25 year contract / 33,000 acres of hazardous fuel.
Planned checker board cuts / islands/ wildlife corridors.
Fire breaks for safe deployment / escape for residents.

## Slide 7: Decks of harvested material

## Slide 8: Summary of steps from fuel harvest to decking
Mechanical harvests / when ground is solid.
Decks placed out of beetle range.
Placed for easy access.

## Slide 9: Wood chips
The first step is to reduce hazardous fuel to a controllable fuel for incineration.

## Slide 10: Summary of conversion of logs to biofuel
Decks transported to fuel yard.
Bunches of trees into grinder / 35 tons per hour.
Chips to storage and into heated floor bin.
Cork screw feeders/ on to conveyer / metered pre-fire bin/ into fire pit.

## Slide 11: Biomass boiler at work.

## Slide 12: Biomass boiler at work continued…
Chips incinerated at 1600 degrees.
Water heated and sent to buildings.
Steam to low speed turbine / to generator (75 KW capacity)

## Slide 13: Benefits and savings to Tok School.
Fossil fuel off / bio fuel on / savings in excess of $200,000.00 per yr.
Electricity balanced load with AP&T / sent to school / in excess of 40 kw.

## Slide 14: Greenhouse
100 ft by 40 ft
slide9

## Slide 15
Processing - to other schools
Warmed beds
Early Planting
Harvest

## Slide 16: Forest Energy for heat, electricity, and food
Kids follow every part of the process in their learning.

## Slide 17: Forest Energy for heat, electricity, and food
School campus is striving to be net zero.

## Slide 18: Forest Energy for heat, electricity, and food
When hazardous spruce fuel helps grow fresh food.

## Slide 19: Forest Energy for heat, electricity, and food
When heavy carbon fuel is replaced by carbon neutral fuel.

## Slide 20: Forest Energy for heat, electricity, and food
When air quality is significantly improved.

## Slide 21
The people of Tok and our School District thank the Legislature for their support of our vision

## Slide 22: Where adults and their children understand how to use our natural forest energy to convert a menace into a meal