## Slide 1
Presentation to the State of Alaska
House Resources Committee
Anchorage, November 1, 2011
Great Bear Petroleum Update

## Slide 2: Regionally Vested Lease Holders The Solution to Alaska’s Grand Challenge Likely Lies on this Map

## Slide 3: North Alaska Shale Resource Play Realization: Challenges and Business Development Opportunities
Gravel Supply: Regionally available
Water Supply: Extensive subsurface brackish aquifer sources
Sand (Proppant) Supply: Intra-State opportunity and global suppliers
Gathering Systems (Tanks/Trucks or Pipelines or Both): Long term, skilled employment
Fluid Disposal/Recycling: Existing and new facilities
Gas use/disposal in area: Power generation, liquids and longer term gas line export
Surface Impacts/Dust and Emissions: AC Rigs and multi-well development pads
Centralized Service Area with power source: Modular startup transitioning to centralized
Power distribution – Stand alone per pad; through power lines: “Utility” grid corridors
Use of Insulation and composite pads to extend ice pads and roads: Not fit for development
Staging area for pipe, equipment, housing, warehousing: Existing facilities and purpose built
Road and bridge requirements: Design to minimize surface impact
Fuel Refining, Storage and Distribution: Existing facilities and custom
Drinking Water Supply: Multiple options identified included desalination of subsurface water
Sewage Treatment/Disposal: Existing and custom in-field facilities planned
Trucking Impacts: Maximize development design efficiencies
Challenges are Opportunities that inspire and drive innovation

## Slide 4: Plan of Development A Staged Development Approach
Phase 1
Proof of Concept (Data Collection and Play Tests)
Vertical wells with horizontal sections Vertical wells to be drilled to Shublik, cored through all 3 main shales Multistage frac tests are planned
Proof of Concept
Pilot Plant (Trucking Operations)
Pilot Development- 1 Year Production Profile
Development Corridor #1
Full Field Development (Corridor Expansion)
2011-2012
2012
2013
2014
2015
Phase 2
Pilot Production (Micro-Processing Module Approach)
Gravel pad (up to 24 wells) Up to 2 production modules (5,000 to 10,000 BOPD each) Facilities (drill slots, yard piping) Pipeline to PS1 Pump station tie-in Power Gas compression Tanks Water disposal Road
Phase 3
Full Development (Production Ramp-Up)
Create Development Corridor 8 pads (192 wells) 1 Central Processing Unit Tactical growth east and west from Development Corridor Targeting 1 new Development module per year
Planning for success and participating in securing Alaska’s future
Successful regional development
offers compounding benefits for
Alaska

## Slide 5: Plan of Development Proof of Concept – Dual Multi Well Programs
2 “Proof of Concept” work programs occurring simultaneously
  Service Co-led program
  Great Bear-led program
Ascertain the productive capacity of the formations
Determine processing requirements for oil, water and gas
Drilling, coring, fracture stimulation and evaluation of vertical & horizontal wells
Utilize disturbed gravel on existing spur roads off the Dalton Highway
Permitting underway at 6 locations
Evaluate reservoir characteristics
Evaluate mechanical properties from core
Determine in-situ stress
Well design (vertical/horizontal/multi-lateral)
Completion design (liner/cement/stimulation)
TAPS
Service Co Proof of Concept Area
Great Bear
Proof of Concept Area

## Slide 6: Plan of Development Phased Development Approach – 3 Main Phases
1
Key Principles
Initially focus activity adjacent to Dalton Highway to minimize new surface impacts and maximize efficiencies
Phased approach to better understand reservoir performance
Establish production potential and then optimize operations (MPU vs CPF)
Accelerate full development eastwards and westwards of Development Corridor. F- full CPF concept
TAPS
Pilot Plant (MPU)
Trucking 5 – 10,000 BOPD
Up to 24 Wells
Pump Station (~ 10 miles)
Great Bear Pipeline
Multi-Pad build out connected by Great Bear pipeline to TAPS
1
2
Initial Development Corridor
3
Full field development fanning out from initial Development Corridor

## Slide 7: Development Corridor Schematic Phased Development Fanning Out From Corridor
Create Development Corridor away from Dalton Highway
Move from trucking operations to pipelines to PS1
Phase from MPU to CPF concept
Each pad manifold building contains single well test separation facilities with associated metering and gas lift distribution
Production piped to CPF which is combined with production from other pads
Oil, gas, water and sediment separated at the CPF and tied into TAPS
Water disposed down dedicated Class II liquid disposal well and produced gas compressed on site and used for power (conservative case assumes excess volume piped to Prudhoe)
8 pads, with 24 wells/pad = 192 wells
Central processing facility
  Field power generation
  Liquid disposal
  Major camp office/warehouse
  Series of divert tanks
  Infield roads/power/telcommunications
  Gas compression
20 mile 12” oil pipeline
20 mile 4” gas line to Prudhoe Bay
Connected PAD system
Ultimately increase production to greater than 100,000 BOPD peak per corridor
1
Development Corridor
CPF
8
7
6
5
4
3
2
Pump Station (10 miles)
1

## Slide 8: Drilling and Completion Operations Safety and Environmental
Safety Management System in place
Site Specific Safety Plan will be written
All onsite workers will be certified as required
Safety briefings will be performed before each task
The North Slope is one of the safest working environments in the world
All systems will be self-contained
The target will be zero fluid discharge
Every fluid drop will be reported and removed for disposal
ACS will be employed to respond to potential large spills
Extra booms and spill cleanup equipment will be available
All workers will be environmentally trained
Regulatory Spill Plan has been submitted
Safety
Environmental
Note: Our Safety Manager or Drilling Manager can go into as much detail as required.
We are committed to operating in a safe, environmentally responsible manner and desire to be recognized as a great corporate citizen by the State and the communities where we do business.