## Slide 1
Renewable Energy Fund Program Status
Alaska Legislature
Juneau
February 27, 2012
Notes: Humpback cr hydro 1250 kW

## Slide 2
Renewables and other Projects
5-Year State Funds

## Slide 3: RE Fund Grant Status Feb 17, 2012
Round | I | II | III | IV | V | Total
Applications Received | 112 | 118 | 123 | 108 | 97 | 558
Projects Funded | 79 | 30 | 25 | 74 | tbd | 208
Grants in Place | 72 | 29 | 19 | 49 | 0 | 165
Grants Completed | 23 | 4 | 0 | 0 | 0 | 27
Grants Cancelled | 5 | 1 | 3 | 0 | 0 | 9
Amount Requested ($M) | $453.8 | $293.4 | $223.5 | $123.1 | $132.9 | $1,226.7
AEA Recommended ($M) | $100.0 | $36.8 | $65.8 | $36.6 | $43.2 | $282.4
Appropriated ($M) | $100.0 | $25.0 | $25.0 | $26.6 | tbd | $176.6
Cash Disbursed ($M) | $54.9 | $17.1 | $6.2 | $2.6 | $0 | $80.8
Match provided ($M) | $20.7 | $22.6 | $10.5 | $34.6 | tbd | $88.4
Other Contributions ($M) | $9.2 | $1.6 | $0.8 | $14.5 | tbd | $26.1
Can be reallocated ($M) | $0 | $0 | $0.2 | $0 | $0 | $0.2
Notes: 208 funded projects
165 grants in place
Strong commitment from the Parnell administration for Renewable projects

## Slide 4: RE Fund Drawdown Outlook
Notes: 208 funded projects
165 grants in place
Strong commitment from the Parnell administration for Renewable projects

## Slide 5: RE Fund Project Completion
Notes: 208 funded projects
165 grants in place
Strong commitment from the Parnell administration for Renewable projects

## Slide 6
Pre-construction Projects (R1-4)

## Slide 7
Construction Projects (R1-4)

## Slide 8
Funding Allocation by
($ x million, Rounds I – IV)
PCE vs Non-PCE
Heat vs Power

## Slide 9
Notes: Speaking to KEA they have just prepared a briefing paper, apparently on the request of the Governor’s office. It concludes KEA is saving approximately $0.105/kWh at $2.60/gal fuel. I have attached it.
Since this savings figure applies to only kWh produced by wind and includes depreciation, O&M, and other non-fuel costs, it is not comparable to AVEC figures, which apply to all kWh produced by the Toksook power system and address only fuel cost displacement. More comparable is Kodiak Electric’s separate estimate that the Pillar Mt project saves approximately $0.016/kWh for every kWh generated by the utility (including diesel and hydro) due to decreased diesel consumption assuming $2.60/gal fuel.
AVEC estimates that its 300 kW wind system in Toksook Bay completed in 2007 saves customers (before PCE) approximately $0.04/kWh in reduced diesel fuel costs. A recent capacity increase to 400 kW through the Renewable Energy Fund program is expected to increase savings to $0.055/kWh. An additional $0.02/kWh savings are realized from upgrading efficiency of the diesel system.
AVEC estimates these savings as follows:
Toksook Bay represents an amalgamated project built in 2006-2007 that closed down two power plants in Tununak and Nightmute and installed 300 kW of wind generation along with a new, more efficient power plant. Comparing 2005 data for all three communities with 2009 data for the combined system, we show the following.
Gross generation in 2005 in all three communities was 3.0 million kWh, using 228,855 gallons of fuel – an efficiency of 12.94 kWh/gallon. 2009 generation was 3.3 million kWh (demonstrating normal growth in consumption) with 600,000 kWh generated by wind and 188,769 gallons of fuel used. Gross fuel efficiency is now 14.38 kWh/gallon or 17.48 if wind and diesel generation are combined.
At $3.125/gallon of fuel, the cost of a kWh of electricity in 2009 was 6 cents less than it was in 2005. Approximately 2 cents is due to the higher efficiency of a consolidated power plant and 4 cents to wind displacement. A fourth wind turbine installed in 2010 is expected to increase wind savings by 1.5 cents, equating to a total cost reduction of 7.5 cents. As the cost of fuel increases, each dollar increase in the cost of fuel equates to wind savings of an additional 1.9 cents/kWh.
Looked at from another perspective, had the project never been built, the 3.3 million kWh generated in 2009 would have required 255,023 gallons of diesel fuel to generate, so the project displaced 66,254 gallons of fuel. At $3.125 a gallon, this would have equated to an additional fuel cost of 6.27 cents per kWh.
Clearly, if the price of diesel increases, savings increase. AEA/ISER’s latest fuel price projections, based on USDOE forecasts, assume that diesel prices in Toksook Bay will increase to $4.67/gal (in 2010$) by 2030. At this fuel price savings due to wind energy would increase proportionately to $0.082/kWh.
Note that this very simple analysis does not consider all factors like operation and maintenance costs of the diesel and wind system components, changes in diesel system efficiency due to wind integration, and availability of waste heat from diesel generation and/or excess wind energy. These and other factors are modeled during system design. But actual savings are best determined by assessing real data from operating systems. Last spring UA Center for Energy and Power prepared a report on system performance and economics, but concluded that additional data is necessary. AEA is requiring such detailed data from utilities that receive RE Fund grants.

## Slide 10: Cost of Scheduled Construction Projects, Rounds I – IV
 | Million
RE Fund Grants | $123.3
Other State Funds | 22.9
Non-state and Local | 218.7
TOTAL | $364.9

## Slide 11: Energy production and diesel cost savings-2011
Includes projects in operation in January 2011 or before.
Tok Wood Heating project shut down June-Dec for steam turbine installation.
Nome Banner Peak wind project is privately owned. The RE Fund paid only for the intertie.
Notes: Bering Straits Native Corp and Sitnasauk own the 1.2 MW wind farm. Nome Joint Utilities proposed 1.8 MW wind farm plans to use the same intertie.

## Slide 12: Challenges/Opportunities
Focus on the entire energy system
  Reliable, efficient diesel systems first
  Reduce demand through EE
Deliverables
  Reduce and stabilize costs to residents
  Displace diesel
  Assist in project development
Monitor technical and economic performance

## Slide 13: Thank you.
Alaska Energy Authority
813 West Northern Lights Boulevard
Anchorage, Alaska 99503
www.akenergyauthority.org